## Slide 1: FIELD MEDICAL ASSISTANT COURSE (FMAC)
MODULE 05:
TACTICAL TRAUMA ASSESSMENT (TTA)

## Slide 2: UNITED NATIONS TACTICAL COMBAT CASUALTY CARE (UN TCCC)
ROLE-BASED TRAINING SPECTRUM
ROLE 1 CARE
NONMEDICAL PERSONNEL
Buddy First Aid
Field Medical Assistant
MEDICAL PERSONNEL
Paramedic
Nurse
Doctor
You are HERE

## Slide 3
TERMINAL LEARNING OBJECTIVE
TO6 Given a combat peacekeeping or non-combat peacekeeping scenario, perform Tactical Field Care in accordance with UN TCCC Guidelines
    EO29 Demonstrate the techniques used to assess a casualty for responsiveness.
    EO30 Identify the common causes of altered mental status in combat peacekeeping or non-combat peacekeeping environments
    EO31 Identify the importance of disarming and securing communications equipment of a casualty with altered mental status
    EO32 Identify the importance and techniques of communicating with a casualty in TFC
    EO33 Demonstrate communicating with a casualty in TFC
    EO34 Demonstrate application of body substance isolation (BSI) in TFC
    EO35 Demonstrate a TTA in the proper order using the MARCH PAWS sequence in accordance with with UN TCCC Guidelines
    EO36 Demonstrate the appropriate actions and interventions used during a casualty assessment to render aid to the casualty in accordance with UN TCCC Guidelines
STUDENT LEARNING OBJECTIVES

## Slide 4: TACTICAL FIELD CARE
DURING LIFE-THREATENING
MASSIVE BLEEDING #1 Priority
AIRWAY
RESPIRATION
CIRCULATION
HYPOTHERMIA / HEAD INJURIES
MARCH PAWS
AFTER LIFE-THREATENING
PAIN
ANTIBIOTICS
WOUNDS
SPLINTING

## Slide 5
TACTICAL TRAUMA ASSESSMENT HOW-TO
TACTICAL TRAUMA ASSESSMENT
Video can be found on DeployedMedicine.com

## Slide 6
COMBAT SPEED TTA
“FIRE FIGHT CONSCIOUS CASUALTY”
TACTICAL TRAUMA ASSESSMENT
“Fire Fight Conscious Casualty”
Video can be found on DeployedMedicine.com

## Slide 7
COMBAT SPEED TTA
“FIRE FIGHT UNCONSCIOUS CASUALTY”
TACTICAL TRAUMA ASSESSMENT
‘Explosion’ Unconscious Casualty”
Video can be found on DeployedMedicine.com

## Slide 8
BODY SUBSTANCE ISOLATION (BSI)
Whenever possible, the responder should don latex-free gloves as a precaution
TACTICAL TRAUMA ASSESSMENT
Notes: Replace Image

## Slide 9
CASUALTY BLOOD SWEEP
Your initial casualty evaluation should be a rapid head-to-toe check for any unrecognized life-threatening bleeding
Check the neck, axillary (armpit), inguinal (groin)
Check the legs, arms, abdomen, chest (in a raking motion) and back
Notes: Replace images

## Slide 10
QUICKLY IDENTIFY
MASSIVE, LIFE-THREATENING BLEEDING
BRIGHT RED BLOOD
is pulsing or spurting, or
there is steady bleeding
from the wound
MASSIVE BLEEDING
Overlying clothing or ineffective
bandaging is becoming
SOAKED WITH BLOOD
BRIGHT RED BLOOD
is pooling on the
ground
AMPUTATION of
the arm or leg
M A R C H
IMPORTANT! Casualties with
severe injuries can bleed to
death in as little as 3 minutes
Notes: Replace images

## Slide 11
HEMORRHAGE CONTROL
Assess for other sources of hemorrhage, and control all life-threatening bleeding
MASSIVE HEMORRHAGE CONTROL IN TFC
If not already done, where appropriate, use a TFMA recommended limb tourniquet (TQ) to control life-threatening external hemorrhage, applying it 2-3 inches above the source of bleeding, directly on the skin
Reassess CUF interventions, and If bleeding is not controlled with the first TQ, apply a second TQ side-by-side with the first
Notes: Replace images

## Slide 12
IDENTIFYING OBSTRUCTED AIRWAY
IMPORTANT! Remove any
visible objects, but do not
perform a blind finger sweep
AIRWAY MANAGEMENT
SIGNS AND SYMPTOMS AIRWAY MAY BE BLOCKED:
Casualty is in distress and indicates they can’t breathe properly
Casualty is making snoring or gurgling sounds
Visible blood or foreign objects are present in the airway
Maxillofacial trauma (severe trauma to the face) is observed
M A R C H
Notes: Replace images

## Slide 13
IN A CASUALTY WITHOUT AN AIRWAY
OBSTRUCTION, YOU CAN PERFORM
THE FOLLOWING MANEUVERS:
If you suspect that the casualty has suffered a neck or spinal injury, use the jaw-thrust method
OPENING THE AIRWAY
M A R C H
Unconscious casualty's tongue may have relaxed, causing the tongue to block the airway by sliding to the back of the mouth and covering the opening to the
Windpipe
HEAD-TILT CHIN-LIFT
JAW THRUST
Notes: Replace images

## Slide 14
MANAGING THE AIRWAY
OPENING THE AIRWAY
M A R C H
IF the casualty is breathing on their own but unconscious or semiconscious AND there is no airway obstruction, further airway management is best achieved with a nasopharyngeal airway (NPA)
An NPA can be used on a conscious or unconscious casualty to help open/maintain an open airway
Notes: Replace images

## Slide 15
MANAGEMENT/RECOVERY POSITION
MANAGING THE AIRWAY
M A R C H
Casualties with severe facial
trauma can often protect
their own airways by sitting
up and leaning forward
Assist a conscious casualty
by helping them assume any
comfortable sitting-up
position that ALLOWS THEM TO BREATH EASILY
For an unconscious casualty
not in shock, place them into
the RECOVERY POSITION
Notes: Replace images

## Slide 16
RESPIRATIONS
TACTICAL TRAUMA ASSESSMENT
M A R C H
Breathing rate
(Monitor respirations)
Level of consciousness
Notes: Replace images

## Slide 17
LIFE- THREATENING CHEST INJURY
TRESPIRATION ASSESSMENT AND MANAGEMENT IN TFC
M A R C H
If penetrating trauma is found
or identified, apply a chest seal (vented, if available)
Expose the chest to assess for:
Gunshot or shrapnel wound
Blunt-force trauma
Bruising or contusions
Any deformities of the chest
Notes: Replace images

## Slide 18
REASSESS TREATMENTS
CIRCULATION
M A R C H
Reassess ALL treatment
for Massive hemorrhage
Reassess Airway
Reassess Respirations
M
R
A
Notes: Replace images

## Slide 19
GENERAL INDICATOR OF SHOCK
CIRCULATION
M A R C H
Mental confusion
Rapid breathing
Sweaty, cool, clammy skin
Pale/grey skin
Weak or absent radial pulse
Nausea
Excessive thirst
Previous severe bleeding
SIGNS AND SYMPTOMS OF SHOCK INCLUDE:
Notes: Replace images

## Slide 20
HYPOTHERMIA PREVENTION
HYPOTHERMIA
M A R C H
Place the casualty on an
insulated surface as soon
as possible
Hypothermia is much easier to prevent than to treat! Begin hypothermia prevention as soon as possible
Decreased body temperature interferes with blood clotting and increases the risk of bleeding
Blood loss can cause a significant drop in body temperature, even in hot weather
REMEMBER:
Hypothermia is an issue
even in hot environments
and must be prevented
Notes: Replace images

## Slide 21
IF A PENETRATING EYE INJURY IS NOTED
OR SUSPECTED
EYE INJURIES
Do not cover both eyes unless both eyes are injured
In the absence of an eye shield, consider using tactical eyewear
Notes: Replace images

## Slide 22
WOUND MEDICATION PACK (WMP)
PENETRATING INJURIES
Acetaminophen
is used for pain
management
Meloxicam can give
significant pain relief
and will not alter the
casualty’s mental
status
Moxifloxacin
contains oral
antibiotic medication
MARCH
PAWS
MARCH
PAWS
Remember:
Medics carry medications
Document all medications administered on the UN Casualty Card
Notes: Replace images

## Slide 23
INSPECT AND ADDRESS KNOWN WOUNDS
TACTICAL FIELD CARE GUIDELINES
Dress all known wounds and then assess all applied
bandages for:
Increased pain
Skin discoloration
Irregular pulse
If any of these conditions are found, they might indicate an emergency!
Ensure the applied bandage isn’t too tight; loosen as needed while keeping the bleeding controlled
DO NOT EVER APPLY IT AND FORGET IT!
MARCH PAWS
Notes: Replace images

## Slide 24
BURN CARE
SECONDARY INJURIES
Be sure to assess MARCH before burn care
EXTRACT
Extract from burning vehicle, building, or area
STOP THE BURNING PROCESS
COVER
Cover the burn area with dry, sterile dressings for general burns
WHITE PHOSPHORUS = WET DRESSING
Eliminate wound contact with oxygen
Notes: Replace images

## Slide 25
ASSESS FOR A FRACTURE
SECONDARY INJURIES
CLOSED FRACTURE
OPEN FRACTURE
WARNING SIGNS
OF A FRACTURE:
Significant pain and swelling
An audible or perceived “snap”
Different length or shape of limb
Loss of pulse or sensation in the injured arm or leg (check pulse before and after treatment)
Crepitus (hearing a crackling or
popping sound under the skin)
Notes: Replace images

## Slide 26
COMMUNICATION
TACTICAL FIELD CARE
Communicate with the casualty and if possible
Encourage
Reassure
Explain care each step of the way
Communicate with tactical leadership as soon as possible with status and evacuation requirements throughout casualty treatment as needed
COMMUNICATE WITH
EVACUATION AND
MEDICAL ASSETS
Communicate with the evacuation system to coordinate CASEVAC using the 4-Line CASEVAC request
Keep the Casualty Card
Notes: Replace images

## Slide 27
PHASE 3: TACTICAL EVACUATION CARE
TACTICAL EVACUATION
CASUALTY MONITORING
Continue to reassess and monitor casualty
CASUALTY PREP
Secure items
Prep litter
Prep evac equipment
Pack casualty
PRE-EVAC PROCEDURES
Complete Casualty Card
COMPLETE MIST
REPORT
M Mechanism of injury
I Injuries
S Symptoms
T Treatment
EVAC REQUEST
Use 4-Line format

## Slide 28
TRAINER-LED DEMONSTRATION
Tactical Trauma Assessment

## Slide 29
SUMMARY
We defined Tactical Trauma Assessment
We discussed assessing the casualty using MARCH PAWS
We discussed proper communication and documentation
TACTICAL TRAUMA ASSESSMENT

## Slide 30
CHECK ON LEARNING
During which phase of care is the TTA performed?
What pneumonic is used to prioritize care during the TTA?
What is a blood sweep?

## Slide 31
ANY QUESTIONS?